## Slide 1: Measurement Standard Operating Procedure
Project: amazon
Part Name: ASSY, DEVICE, CARNIVAL
Part Number: 05-108353 Rev: 02
Prepared by: S. T. Pan Date: 2026/06/06
Checked: Y. H. Ning
制作: f2160112
Notes: ----- Meeting Notes (9/4/13 09:43) -----
add column for cpk vs in-process
remove datums

## Slide 2: Contents
Contents | Note | Page
Revision History |  | Page 3
Summary |  | Page 4
Measurement Equipment | CMM, OMM, HG | Page 5~7
Fixture Structure |  | Page 8
Datum Establishment OMM1& Measurement Description |  | Page 9~11
Datum Establishment OMM2& Measurement Description |  | Page 12~13
Datum Establishment OMM3& Measurement Description |  | Page 14~15
Datum Establishment OMM4& Measurement Description |  | Page 16~17
Datum Establishment OMM5& Measurement Description |  | Page 18
Datum Establishment OMM6& Measurement Description |  | Page 19
Datum Establishment CMM1& Measurement Description |  | Page 20
Notes: ----- Meeting Notes (9/4/13 09:43) -----
add column for cpk vs in-process
remove datums

## Slide 3: Revision History
Rev | Zone | Description Of Revision | APPROVED BY | DATE
01 |  | FIRST RELEASE | CARL | 2026/01/08
02 |  | UPDATE FAI06-1,FAI06-2,FAI11 | CARL | 2026/05/28

## Slide 4: Summary
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI01 |  | 9.35 | 0.30 | -0.30 | OMM | Distance | / | S1D4 | 
FAI02 |  | 91.50 | 0.20 | -0.20 | OMM | Length | / | S1C4 | 
FAI03 |  | 3*21.10 | 0.20 | -0.20 | OMM | Width | / | S1B4 | W1,W2,W3
FAI04 |  | 2*0.21 | 0.10 | -0.10 | OMM | GAP | / | S1B3 | 
FAI05 |  | 2*0.21 | 0.10 | -0.10 | OMM | GAP | / | S1B3 | 
FAI06-1 |  | 9*0.05 | 0.10 | -0.10 | OMM | STEP | / | S1B2 | S2~S10
FAI06-2 |  | 3*0.00 | 0.10 | -0.10 | OMM | STEP | / | S1D1 | S1,S11,S12
FAI7 |  | 3*14.50 | 0.40 | -0.40 | CMM | Height | / | S1B2 | H1,H2,H3
FAI8 |  | 12*0.05 | 0.10 | -0.05 | OMM | GAP | / | S1D1 | G1~G12
FAI9 |  | 2*0.35 | 0.20 | -0.20 | OMM | GAP | / | S1C1 | 
FAI10 |  | 2*0.35 | 0.20 | -0.20 | OMM | GAP | / | S1C1 | 
FAI11 |  | 0.28 | 0.26 | -0.26 | OMM | Distance | / | S2C2 | 
Notes: ----- Meeting Notes (9/4/13 09:43) -----
add column for cpk vs in-process
remove datums

## Slide 5
CMM MANUFACTURER: Hexagon
CMM MODEL: PM-T8106
PRECECISON: ±(2.8+L/300)μm
PROBE T1
  PROBE MANUFACTURER: Renishaw
  PROBE MATERIAL: Tungsten carbide
  PROBE TYPE: Cylindrical needle
  PROBE DIAMETER: Ø0.5x15.3mm
  SHAFT LENGTH: 20mm
PROBE T2
  PROBE MANUFACTURER: /
  PROBE MATERIAL: /
  PROBE SHAPE: /
  PROBE DIAMETER: /
  SHAFT LENGTH: /
NOTE: Select probe configuration based on measurement situations
Coordinate Measuring Machine(接触式三次元)
Measurement Equipment - CMM
Notes: 5

## Slide 6
OMM MANUFACTURER: Foxconn
OMM MODEL: Power Metro 3000
MEASURING RANGE: X=300mm, Y=300mm, Z=200mm
MAX MAGNIFICATION: 3X (Screen Magnification: 90X)
PRECECISON: U1xy:(1.5+L/333)μm; U1z:(3.0+L/250)μm;
LIGHTING CONDITION: Ring Light, Profile Light, Coaxial Light
Lighting Condition
Optical Coordinate Measuring Machine(影像三次元)
Measurement Equipment - OMM
Notes: 6

## Slide 7
HG MANUFACTURER: Nikon
HG MODEL: MF-1001
MEASURING RANGE: 0.0001~100.0000mm
RESOLUTION: 0.0001mm
TOUCH FORCE: /
Height Gauge(电子高度计)
Measurement Equipment - HG

## Slide 8
1).樣品裝夾如下圖所示。
Fixture Structure
Fixture & Positioning method(夹具及定位方法):
装夹前
装夹后
Notes: 8

## Slide 9
Datum Establishment
OMM Build Datum Alignment 1
Measurement equipment(测量设备): OMM
Clamping instructions(裝夾说明): /
Magnification/ Lighting condition(倍率/光源): 1x / Ring Light
Datum Setup(基准建立):
1.按照下(图1)所示装夹产品, 并放置于设备平台上。
2.在产品表面对焦取点测量平面PL1(Z1~Z4), 在产品边缘取点P1~P5。
3.P4&P2构建线L1, P5&P3构建线L2, L1&L2构建中线L3。
4.将PL1摆正Z轴, L3旋转至Y轴, 设定PL1为Z轴原点, 设定L3为X轴原点, 设定P1为Y轴原点。
P1
Z1
P2
P3
P5
P4
(图1)
Z2
Z4
Z3
Notes: 9

## Slide 10
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI01 |  | 9.35 | 0.30 | -0.30 | OMM | Distance | / |  | 
FAI02 |  | 91.50 | 0.20 | -0.20 | OMM | Length | / |  | 
FAI03 |  | 21.10 | 0.20 | -0.20 | OMM | Width | / |  | W1,W2,W3
Measurement Description
Measurement equipment(测量设备): OMM
Magnification/ Lighting condition(倍率/光源): 1x / Ring Light
Measurement Datum (测量基准): OMM Build Datum Alignment 1
Measurement description(测量描述):
1).在X=0mm的位置取点P1, P6。
2).在Y=-8.00mm的位置取点P2, P3。
3).在Y=-45.75mm的位置取点P4, P5。
4).在P6的Y轴座标值+8.00mm处取点P7, P8。
5).FAI01: 输出P1的Y向座标值。
FAI02: 输出P6的Y向座标值。
FAI03-W1: 输出{P2&P3}的X向距离。
FAI03-W2: 输出{P4&P5}的X向距离。
FAI03-W3: 输出{P7&P8}的X向距离。
POS | X | Y
P1 | 0 | /
P2 | / | -8.00
P3 | / | -8.00
P4 | / | -45.75
P5 | / | -45.75
P6 | 0 | /
P7 | / | P6.Y+8.00
P8 | / | P6.Y+8.00
P2
P3
P8
P7
(图1)
P4
P5
P6
P1
Notes: 10

## Slide 11
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI06-1 |  | 0.05 | 0.10 | -0.10 | OMM | STEP | / |  | S2~S10
FAI06-2 |  | 0.00 | 0.10 | -0.10 | OMM | STEP | / |  | S1,S11,S12
Measurement Description
Measurement equipment(测量设备): OMM
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Measurement Datum (测量基准): OMM Build Datum Alignment 1
Measurement description(测量描述):
1.1).如下(图1)所示, 在S2处取点P1, P2。
1.2).FAI06-1-S2: 输出{P1&P2}的X向距离。
1.3).用相同方法测量S3, S4, S6, S8~S10, S1, S11, S12的位置。 。
2.1).将S4设为X原点, S6设为Y原点, OMM基准1旋转45度, 在
S5处取点P3, P4 。
2.2).FAI06-1-S5: 输出{P3&P4}的Y向距离。
2.3).用相同方法测量S7的位置。
S2
S10
S8
S4
(图1)
S3
S9
S6
S1
S2取点位置
S11
S5
S7
S12
P1
P2
y
x
P3
P4
S5取点位置
Notes: 11

## Slide 12
OMM Build Datum Alignment 2
Measurement equipment(测量设备): OMM
Clamping instructions(裝夾说明): /
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Datum Setup(基准建立):
1.按照下(图1)所示装夹产品, 并放置于设备平台上。
2.在产品表面对焦取点Z1, 在产品边缘取点P1~P3 。
3.P1&P2构建线L1, 将L1旋转至Y轴, 设定Z1为Z轴原点, 设定L1为X轴原点, 设定P3为Y轴原点。
Datum Establishment
(图1)
Z1
P2
P1
P3
P1, P2
Notes: 12

## Slide 13
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI08 |  | 0.05 | 0.10 | -0.05 | OMM | GAP | / |  | G2~G5
/ |  |  |  |  |  |  |  |  | 
Measurement Description
Measurement equipment(测量设备): OMM
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Measurement Datum (测量基准): OMM Build Datum Alignment 2
Measurement description(测量描述):
1).按照(图1)所示, 在G2(Y=-8.00mm)的位置取点P1, P2 。
2).FAI08-G2：输出{P1&P2}的X向距离。
3).用同样方法测量G3, G4, G5的位置。
POS | Y
G2 | -8.00
G3 | -45.75
G4 | -83.50
G5 | -90.00
P1
P2
G2~G5
G2
G3
G4
G5
(图1)
Notes: 13

## Slide 14
OMM Build Datum Alignment 3
Measurement equipment(测量设备): OMM
Clamping instructions(裝夾说明): 如(图1)所示
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Datum Setup(基准建立):
1.按照下(图1)所示装夹产品, 并放置于设备平台上。
2.如图所示在产品表面对焦取点Z1, 在产品边缘取点P1~P3。
3.P1&P2构建线L1, 将L1旋转至Y轴, 设定Z1为Z轴原点, 设定L1为X轴原点, 设定P3为Y轴原点。
Datum Establishment
(图1)
Z1
P2
P1
P3
P1, P2
Notes: 14

## Slide 15
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI08 |  | 0.05 | 0.10 | -0.05 | OMM | GAP | / |  | G7~G10
FAI09 |  | 0.35 | 0.20 | -0.20 | OMM | GAP | / |  | 2x
FAI10 |  | 0.35 | 0.20 | -0.20 | OMM | GAP | / |  | 2x
Measurement Description
Measurement equipment(测量设备): OMM
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Measurement Datum (测量基准): OMM Build Datum Alignment 3
Measurement description(测量描述):
1.1).按照(图1)所示,在G10(Y=-8.00mm)的位置, 取点P1, P2;
FAI08-G10：输出{P1&P2}的X向距离。
1.2).用相同方法测量G9, G8, G7的位置。
2.1).在(图2)所示的位置取点P3~P10;
FAI09-1 ：输出{P3&P4}的Y向距离。
FAI09-2 ：输出{P5&P6}的Y向距离。
FAI10-1 ：输出{P7&P8}的X向距离。
FAI10-2 ：输出{P9&P10}的X向距离。
POS | Y
G7 | -90.00
G8 | -83.50
G9 | -45.75
G10 | -8.00
P4
P7
P8
P9
P10
P5
P6
P3
(图1)
G10
G9
G8
P1
P2
(图2)
G7
G7~G10
Notes: 15

## Slide 16
Datum Establishment
OMM Build Datum Alignment 4
(图1)
Measurement equipment(测量设备): OMM
Clamping instructions(裝夾说明): 如(图1)所示裝夾
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Datum Setup(基准建立):
1.按照(图1)所示竖立装夹产品并放于机台上, 在产品HDMI表面对焦测量平面PL1(Z1~Z4);
2.在产品边缘取点P1~P4。P2&P3构建线L1, P1&P4构建中点M1;
3. PL1摆正Z轴, 将L1旋转至X轴, 设定PL1为Z轴原点, M1为X轴原点, L1为Y轴原点。
Z1
P1
P2
P3
P4
Z4
Z3
Z2
Notes: 16

## Slide 17
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI04 |  | 0.21 | 0.10 | -0.10 | OMM | GAP | / |  | 2x
FAI05 |  | 0.21 | 0.10 | -0.10 | OMM | GAP | / |  | 2x
FAI08 |  | 0.05 | 0.10 | -0.05 | OMM | GAP | / |  | G12
Measurement equipment(测量设备): OMM
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Measurement Datum (测量基准): OMM Build Datum Alignment 4
Measurement description(测量描述):
1).按右图所示, 取点P1~P8,
FAI04-1：输出{P1&P2}的Y向距离
FAI04-2：输出{P3&P4}的Y向距离
FAI05-1：输出{P5&P6}的X向距离
FAI05-2：输出{P7&P8}的X向距离
2).按右图所示, 取点P9, P10,
FAI08-G12 ：输出{P9&P10}的Y向距离
Measurement Description
P9
P10
P1
P2
P5
P6
P4
P3
P7
P8
ALL
ALL
(图1)
G12
Notes: 17

## Slide 18
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI08 |  | 0.05 | 0.10 | -0.05 | OMM | GAP | / |  | G6
/ |  |  |  |  |  |  |  |  | 
Measurement equipment(测量设备): OMM
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Measurement Datum (测量基准): 建立OMM基准5
1).按照(图1)所示竖立装夹产品, 并在产品上表面对焦取点Z1。
2).在产品边缘取点P1~P4。P2&P3构建线L1, P1&P4构建中点M1。L1旋转至X轴, 设定M1为X轴的原点, 设定L1为Y的原点, 设定Z1为Z的原点。
Measurement description(测量描述):
1).在OMM基准5下,取点P5, P6。
FAI08-G6 ：输出{P5&P6}的Y向距离。
Datum Establishment & Measurement Description
(图1)
P1
P2
P3
P4
P5
P6
Z1
G6取点位置
Notes: 18

## Slide 19
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI11 |  | 0.28 | 0.26 | -0.26 | OMM | Distance | / |  | H1,H2,H3
/ |  |  |  |  |  |  |  |  | 
Measurement equipment(测量设备): OMM
Magnification/ Lighting condition(倍率/光源): 2x / Ring Light
Measurement Datum (测量基准): 建立OMM基準6
1).按照右图所示, 先将数据线插入产品接口, 再平放机台上。在产品表面对焦测量點Z1, 在产品标示位置測量点P1~P3, P1&P2構建線L1。
2).L1旋轉至Y軸, 設置Z1為Z=0, 設置L1為X=0, 設置P1為Y=0。
Measurement description(测量描述):
在OMM基準6下：
1).如(图1)所示, 在产品上測量點P4, 在数据线上测量点P5。
2).FAI11 ：输出{P4&P5}的X向距离。
Datum Establishment & Measurement Description
Z1
P3
P2
P1
P4
P5
Notes: 19

## Slide 20
No. | SPC Callout | Nominal | +Tol | -Tol | Measurement Method | Description | Fixture No. | Drawing Location | Remark
FAI07 |  | 14.50 | 0.40 | -0.40 | CMM | Height | / |  | W1,W2,W3
/ |  |  |  |  |  |  |  |  | 
Measurement equipment(测量设备): CMM
Magnification/ Lighting condition(倍率/光源): /
Measurement Datum (测量基准): 建立CMM基準1
1).按照(图1)所示, 先将产品置於CMM幾台上, 在垫块的表面測量平面PL1(Z1~Z4)。
2).在产品标示位置測量點P1~P4, P3&P1構建線L1, P4&P2構建線L2, L1&L2再構建中線L3。
3).PL1摆正Z軸, 並設置PL1為Z=0; L3旋轉至Y軸, 設置L3為X=0, 設置P1為Y=0。
Measurement description(测量描述):
在CMM基準1下：
1).如(图1)所示, 在樣品上測量點H1~H3。
2).FAI07-W1:输出{H1&PL1}的Z向距离。
FAI07-W2:输出{H2&PL1}的Z向距离。
FAI07-W3:输出{H3&PL1}的Z向距离。
POS | X | Y
H1 | 0 | -15.00
H2 | 0 | -45.75
H3 | 0 | -76.50
Datum Establishment & Measurement Description
(图1)
Z1
Z2
Z3
Z4
P1
P1
P2
P3
P4
H1
H2
H3
Notes: 20

## Slide 21
End，thanks!