## Slide 1
CBD Calla panel
Automatic assembly line
--- Stick B-side EMI Machine
Jan 23, 2026

## Slide 2
unit：mm
CBD Calla PCBA Assembly Line（New）
Line flow
900
900
800
840
900
900
Automation Assembly Line UPH ：500PCS/H
Automation Assembly Line Dimension ： L 11020mm * W 1500mm * H 1620mm (For reference, according to the actual)
Item | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 4 | 11 | 12 | 13
Equipment | Stick B-side EMI Machine | Point B-side heat dissipation paste Machine | Stick B-side heat sink Machine（Robot） | Pressing machine | Stick B-side foam Machine*2 | Flip Over Machine | Stick T-side EMI Machine | Point T-side heat dissipation paste Machine | Stick T-side heat sink Machine（Robot） | Pressing machine | Stick FSS Machine | Pressing FSS machine | Stick T-side foam Machine*2
New /Old | old | old | old | Gs | old | Gs | old | old | old | Gs | new | Gs | old
CT(S) | 6 | 6 | 6 | 4 | 6 | 6 | 6 | 6 | 6 | 4 | 6 | 4 | 6
Feeding method | reel | Plastic bucket | reel | / | reel | reel | / | Plastic bucket | reel | / | reel | / | reel
Auto machine(new)
Auto machine(old)
600
900
800
840
900
840
900
Auto machine（Guest supply）

## Slide 3
Item | 1 | 2 | 3 | 4 | 5 | 7 | 8 | 9 | 10 | 11 | 12
Equipment | Point B-side heat dissipation paste Machine | Stick B-side EMI Machine | Stick B-side heat sink Machine | Pressing machine | Stick B-side foam Machine*2 | Flip Over Machine | Point T-side heat dissipation paste Machine | Stick T-side EMI Machine | Stick T-side heat sink Machine | Pressing machine | Stick T-side foam Machine*1
New /Old | old | old | old | new | old | Gs | old | old | old | new | old
CT(S) | 4 | 5 | 6 | 3 | 6 |  | 6 | 5 | 6 | 3 | 6
Feeding method | Plastic bucket | reel | reel | / | reel | / | Plastic bucket | reel | reel | / | reel
unit：mm
CBD Cony PCBA Assembly Line（Old）
Line flow
Automation Assembly Line UPH ：500PCS/H
Automation Assembly Line Dimension ： L 9300mm * W 1500mm * H 1620mm (For reference, according to the actual)
900
900
800
840
900
600
900
840
800
900
900
Auto machine(new)
Auto machine(old)
Auto machine（Guest supply）

## Slide 4
Contents
3
unit：mm
Item | Description | DRI
1 | Historical version | Wang hao
2 | Machine performance design | Wang hao
3 | Product Change | Wang hao
4 | Equipment Layout | Wang hao
5 | The key components | Wang hao
6 | Key Fixture Design | Wang hao
7 | Action flow design | Wang hao
8 | Timing diagram | Wang hao

## Slide 5
Version | Description | Date | DRI | Remark
V01 | Initial design version | 2026/01/23 | Wang hao | 
1. Historical version
4
unit：mm

## Slide 6
Purpose | Take out EMI from the Feeder and attach it to the PCBA board B-side
PCBA board | 137.6*199.8mm
Tool | TABLE Load transfer component，Suction nozzle，CCD，Feeder，Actuator
Process | CCD calibration
Process requirements | Alignment tolerance: +/- 0.13mm
UPH requirements | 640PCS
Attach EMI to PCBA board B-side
5
unit：mm
PCBA board
Function:
2. Machine Performance Design
EMI

## Slide 7
3.Product Change
PCBA：
6
unit：mm
184mm
137.6mm
159mm
187.8mm
Cony
Calla
Need to change the image from newst Calla panel design Drw, the dimension from 184mm to 177 mm

## Slide 8
7
unit：mm
4.Equipment Layout
1600mm
 | automatic
CT | 4.5S
UPH | 640PCS
Tricolor lamp
Touch screen
PC
unit：mm
900mm
900mm

## Slide 9
8
4.Equipment Layout
unit：mm
Item | Components
1 | Into the PCBA conveyor line(feed)
2 | Positioning PCBA (Clamping PCBA）
3 | X/Y TABLE Load transfer component (material fetching)
4 | Feeder（Feeding）
5 | Lower CCD (Label compensation position）
6 | Upper CCD (product positioning)
7 | Conveyor line outflowPCBA
7
Conveyor line outflowPCBA
3
X/Y TABLE Load transfer component
(material fetching
4
Feeder（Feeding）
6
Upper CCD
(product positioning)
5
Lower CCD
(Label compensation position）
1
Into the PCBA
conveyor line(feed)
Positioning PCBA
(Clamping PCBA）
2

## Slide 10
unit：mm
4.Equipment Layout
9
5
4
2
Placement head
Lower CCD
Y-axis
1
Feeder
3
X-axis
6
Transport module

## Slide 11
Due to changes in the length
of the PCBA, need to
change the blocking block of
the blocking cylinder
10
5.1 Feed conveyor line
PCBA board positioning process:
1.The PCBA board flows into the conveyor line, and the CX-461A senses that the conveyor line
slows down and blocks the PCBA board from the blocking cylinder.
2.The lifting cylinder is pushed out to position the PCBA board.
5. The key components
PCBA in place deceleration sensor
PCBA blocking cylinder
PCBA jacking cylinder
Motor
PCBA support board
PCBA lifting limit component
138.6mm
Sensor CX-461A
Detect whether the PCBA drives into the conveyor line
Sensor CX-461A
Detect whether the PCBA drives into the conveyor line

## Slide 12
5.1 Feed conveyor line
5. The key components
PCBA board clamping:
1. PCBA board arrives at the assembly position;
2, the block cylinder is blocked out3. At the same time, the support plate rises to support the PCBA board.
11
unit：mm
clamping position
The distance between the connecting plate and the edge of the conveyor line is 0.5mm
The clamp block is in contact with the edge strip of the connecting plate 3.8mm

## Slide 13
5. The key components
5.1 Feed conveyor line
12
unit：mm
B-side jacking plate(A6061)
The TPYE-C port is
5.5mm from the front
of the avoidance slot
5.5mm

## Slide 14
Main structure: sliding table, servo actuator, CCD, suction nozzle
Y-axis transfer | 
Type | ETH14-L32-500-BC-S40-A2
Brand | TOYO
repeatability | ±0.005mm
Position accuracy | ±0.01mm
Travel distance | 500mm
Max speed | 1600mm/s
Work speed | 1280mm/s
Maximum load | 15kg
Work load | 10.5kg
X-axis transfer | 
Type | GTH8-L20-400-BC-S20-C4
Brand | TOYO
repeatability | ±0.005mm
Position accuracy | ±0.01mm
Travel distance | 250mm
Max speed | 1000mm/s
Work speed | 800mm/s
Maximum load | 18kg
Work load | 5kg
13
Z-axis transfer | 
Type | ZRB-MM8-P10-S50-M28-EC
Brand | SCAUTO
repeatability | ±0.01mm
Position accuracy | ±0.02mm
Travel distance | 50mm
Max speed | 200mm/s
Work speed | 150mm/s
Maximum load | 300g
Work load | 50g
unit：mm
5.2 TABLE Load transfer component
5. The key components
X-axis slide table
Servo actuator
Y-axis slide table
Vacuum negative pressure gauge
Suction nozzle
Upper CCD

## Slide 15
14
Y-axis ETH14-L32-500-BC-S40-A2
X-axis GTH8-L20-400-BC-S20-C4
5.2 TABLE Load transfer component
5. The key components
unit：mm

## Slide 16
5.3 Feeder
Feeder | 
category | 120- Pullback marking machine (standard machine)
UPH | 1s/pcs
Diameter of roll | 180mm
Strip width | 44mm
Quantity | Estimated 10K
15
unit：mm
5. The key components
Note: It is recommended that the bidding platform be manually wiped and cleaned with a dust-free cloth once per shift.
Retrieval area
Roll material indication
sensing fiber

## Slide 17
5. The key components
5.4 Upper CCD
unit：mm
layout：
135±10mm
30±10mm
lens：FL-CC1214A-2M
camera：FM-GE500-22M
optical source：HRS-70R60
PCBA
Hardware name | Model | quantity
camera | FM-GE500-22M | 1
lens | RICOH/FL-CC1214A-2M | 1
Close up adaptor | 无 | 0
optical source | 光源/華周/HRS-70R60 | 1
optical source controller | DKZ2-24V-2-AC | 1
Camera mounting orientation | back to the human machine ↑
The distance between the camera surface → the product | 135±10 mm
The distance between the camera surface → optical source | 30±10mm
visual field | 56*42mm
Image pixel size | 2592*1944
Camera single-pixel accuracy | 0.021

## Slide 18
5. The key components
5.4 Lower CCD
unit：mm
layout：
195±10mm
30±10mm
lens：FL-CC3516-2M
camera：FM-GE500-22M
optical source：LRS-90R30
ingredients
Hardware name | Model | quantity
camera | FM-GE500-22M | 1
lens | RICOH/FL-CC3516-2M | 1
Close up adaptor | 5mm | 1
optical source | 光源/華周LRS-90R30 | 1
optical source controller | DKZ2-24V-2-AC | 1
Camera mounting orientation | against sheet metal ↓
The distance between the camera surface → the product | 195±10 mm
The distance between the camera surface → optical source | 30±10mm
visual field | 27*20mm
Image pixel size | 2592*1944
Camera single-pixel accuracy | 0.01

## Slide 19
18
unit：mm
X axis module accuracy | ±0.01
Y axis module accuracy | ±0.01
Z axis module accuracy | ±0.02
Upper CCD Recognition accuracy | ±0.06
Lower CCD Recognition accuracy | ±0.03
Positioning accuracy = X axis module accuracy + Y axis module accuracy + Z axis module accuracy：±（0.01+0.01+0.02）= ±0.04mm；
Placement accuracy = Positioning accuracy + Upper CCD Recognition accuracy + Lower CCD Recognition accuracy ：±（0.04+0.06+0.03）= ± 0.13mm。
5.5 Process requirements
5. The key components

## Slide 20
19
unit：mm
6.Key fixture design
6.1Material fetching mechanism
Suction nozzle
optical source
Upper CCD
ZRB-MM8-P10-S50-M28-EC
（ Rated thrust20N ）

## Slide 21
20
unit：mm
6.Key fixture design
6.1Material fetching mechanism
9mm
2.48mm
EMI
10.07mm
2mm
8mm
Universal structure, built-in spring as placement buffer, placement pressure of 8-16N.
The adsorption surface is customized according to the shape of each excipient

## Slide 22
21
unit：mm
Step1: The PCBA board of the front conveyor line flows in, blocking the cylinder from rising, and the sensor responds in place, and the jacking cylinder rises and clamps the PCBA continuous wrench
Step2: Upper CCD identifies and locates the Mark point of the PCBA
Step6: Blocking the cylinder and jacking cylinder to descend, the PCBA board flows out of the equipment and enters the next process
Step3: The placement head moves to the reclaiming area to absorb EMI
Step5:The placement head is moved to the placement area for placement
Step4:The placement head is moved to the lower CCD to identify EMI
7.Action flow design

## Slide 23
22
UPH≈3600/4.5*0.8=640
Note：80% is estimated OEE, only for UPH calculation. not real product data
unit：mm
Automatic EMI 0.5s/grid |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Product entry into the workspace 產品入工作區 | Running time of the conveyor line is 1.5 seconds 輸送線運轉時間1.5s | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Product positioning 0.5s 產品定位 0.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Take photos of the material collection point 取料點拍照 | Move the slide to the material collection point for 0.5s 滑台移動至取料點 0.5s | 1.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Take photos of the material collection point for 1 second 取料點拍照 1s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Suction nozzle feeding 吸嘴取料 | Left suction nozzle feeding (No.1) for 1.5s 左吸嘴取料（1號） 1.5s |  |  |  |  | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Right suction nozzle feeding (No.2) for 1.5s 右吸嘴取料（2號） 1.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Product photography 產品拍照 | Slide moves to Mark point for 1.5s to take photos 滑台移動至Mark點拍照 1.5s |  |  |  |  |  |  |  |  |  | 1.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Take photos of the discharge point (points 1-10) for 8 seconds 放料點拍照（1-10號點）8s |  |  |  |  |  |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Suction nozzle discharge 吸嘴放料 | Left suction nozzle discharge (No.1) for 1.5s 左吸嘴放料（1號） 1.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Right suction nozzle discharge (No.2) for 1.5s 右吸嘴放料（2號） 1.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Material collection and discharge process 取放料流程 | Move the slide to the material collection point for 0.5s 滑台移動至取料點 0.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 35 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Left suction nozzle feeding (No.3) for 1.5s 左吸嘴取料（3號） 1.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Right suction nozzle feeding (No. 4) for 1.5s 右吸嘴取料（4號） 1.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Move the slide to the discharge point for 0.5s 滑台移動至放料點 0.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Left suction nozzle discharge (No.3) for 1.5s 左吸嘴放料（3號） 1.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Right suction nozzle discharge (No. 4) for 1.5s 右吸嘴放料（4號） 1.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Repeat the above material collection and discharge process 3 times (No. 5-10) for 21 seconds 重複以上取放料流程3次(5-10號) 21s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Product outflow 產品流出 | Cancel product positioning for 0.5s 產品定位取消 0.5s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1.5 |  | 
 | Buffer 1 second after product inflow 產品流入后buffer 1s |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | ## | ## | ## | ## | ## | ## | ## | ##
Cycle time/s | 53.5/12=4.5S | UPH: 3600/4.5*0.8=640 (Pcs) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8. Timing diagram

## Slide 24
Thank you
23