## Slide 1
CBD Calla panel
Automatic assembly line
--- Stick T-side heat sink Machine
Jan 23, 2026

## Slide 2
unit：mm
CBD Calla PCBA Assembly Line（New）
Line flow
900
900
800
840
900
900
Automation Assembly Line UPH ：500PCS/H
Automation Assembly Line Dimension ： L 11020mm * W 1500mm * H 1620mm (For reference, according to the actual)
Item | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 4 | 11 | 12 | 13
Equipment | Stick B-side EMI Machine | Point B-side heat dissipation paste Machine | Stick B-side heat sink Machine（Robot） | Pressing machine | Stick B-side foam Machine*2 | Flip Over Machine | Stick T-side EMI Machine | Point T-side heat dissipation paste Machine | Stick T-side heat sink Machine（Robot） | Pressing machine | Stick FSS Machine | Pressing FSS machine | Stick T-side foam Machine*2
New /Old | old | old | old | Gs | old | Gs | old | old | old | Gs | new | Gs | old
CT(S) | 6 | 6 | 6 | 4 | 6 | 6 | 6 | 6 | 6 | 4 | 6 | 4 | 6
Feeding method | reel | Plastic bucket | reel | / | reel | reel | / | Plastic bucket | reel | / | reel | / | reel
Auto machine(new)
Auto machine(old)
600
900
800
840
900
840
900
Auto machine（Guest supply）

## Slide 3
Item | 1 | 2 | 3 | 4 | 5 | 7 | 8 | 9 | 10 | 11 | 12
Equipment | Point B-side heat dissipation paste Machine | Stick B-side EMI Machine | Stick B-side heat sink Machine | Pressing machine | Stick B-side foam Machine*2 | Flip Over Machine | Point T-side heat dissipation paste Machine | Stick T-side EMI Machine | Stick T-side heat sink Machine | Pressing machine | Stick T-side foam Machine*1
New /Old | old | old | old | new | old | Gs | old | old | old | new | old
CT(S) | 4 | 5 | 6 | 3 | 6 |  | 6 | 5 | 6 | 3 | 6
Feeding method | Plastic bucket | reel | reel | / | reel | / | Plastic bucket | reel | reel | / | reel
unit：mm
CBD Cony PCBA Assembly Line（Old）
Line flow
Automation Assembly Line UPH ：500PCS/H
Automation Assembly Line Dimension ： L 9300mm * W 1500mm * H 1620mm (For reference, according to the actual)
900
900
800
840
900
600
900
840
800
900
900
Auto machine(new)
Auto machine(old)
Auto machine（Guest supply）

## Slide 4
Contents
3
unit：mm
Item | Description | DRI
1 | Historical Versions | Wang hao
2 | Machine performance design | Wang hao
3 | Product Change | Wang hao
4 | Equipment Layout | Wang hao
5 | The key components | Wang hao
6 | Key Fixture Design | Wang hao
7 | Action flow design | Wang hao
8 | Timing diagram | Wang hao

## Slide 5
Version | Description | Date | DRI | Remark
V01 | Initial design version | 2026/01/23 | Wang hao | 
1. Historical Versions
4
unit：mm

## Slide 6
2. Machine performance design
Function ：
PCBA board
Heat sinks*12
5
unit：mm
Attach the heat dissipation sheet*12 to the PCBA board
purpose | Remove the heat dissipator*12 from the label dispenser and attach it to the PCBA board
PCBA board | 137.6*199.8mm
tool | TABLE Transfer components，Nozzle，CCD，Bid dispenser，Actuators
process | CCD calibration
UPH requirements | 900PCS

## Slide 7
3.Product Change
PCBA：
6
unit：mm
184mm
137.6mm
159mm
187.8mm
Cony
Calla
Need to change the image from Calla newest panel design Drw, the W reduce from 184mm to 177 mm

## Slide 8
4. Machine layout
 | automatic | manual
CT | 48.0S | /
UPH | 500PCS | /
7
1630mm
Tricolor lamp
unit：mm
PC
500mm
335mm
165.5mm
287.5mm
Touch screen

## Slide 9
4. Machine layout
8
2
Infeed conveyor line
unit：mm
3
Position the component(Clamp the PCBA board)
5
Bidding machine (feeding)
7
Upper CCD & Reclaiming Assembly(Product positioning ）
6
under CCD components(Label fills ）
4
Robot
8
Buffer after the flow of the conveyor line
item | Process flow
1 | Conveyor line flow buffer
2 | Infeed conveyor line
3 | Position the component(Clamp the PCBA board)
4 | Robot
5 | Bidding machine (feeding)
6 | under CCD components(Label fills ）
7 | Upper CCD & Reclaiming Assembly(Product positioning ）
8 | Buffer after the flow of the conveyor line
1
Conveyor line flow buffer

## Slide 10
4. Machine layout
Infeed conveyor line
1
9
unit：mm
Robot
2
Bid dispenser
4
Under CCD
5
Upper CCD & Reclaiming Assembly
3

## Slide 11
Due to changes in the length
of the PCBA, need to
change the blocking block of
the blocking cylinder
10
5.1 Feed conveyor line
PCBA board positioning process:
1.The PCBA board flows into the conveyor line, and the CX-461A senses that the conveyor line
slows down and blocks the PCBA board from the blocking cylinder.
2.The lifting cylinder is pushed out to position the PCBA board.
5. The key components
PCBA in place deceleration sensor
PCBA blocking cylinder
PCBA jacking cylinder
Motor
PCBA support board
PCBA lifting limit component
138.6mm
Sensor CX-461A
Detect whether the PCBA drives into the conveyor line
Sensor CX-461A
Detect whether the PCBA drives into the conveyor line

## Slide 12
5.1 Feed conveyor line
5. The key components
PCBA board clamping:
1. PCBA board arrives at the assembly position;
2, the block cylinder is blocked out3. At the same time, the support plate rises to support the PCBA board.
11
unit：mm
clamping position
The distance between the connecting plate and the edge of the conveyor line is 0.5mm
The clamp block is in contact with the edge strip of the connecting plate 3.8mm

## Slide 13
5. The key components
5.1 Feed conveyor line
12
unit：mm
T-side jacking plate(A6061)
The size of the
scanner avoidance
slot is 18x40mm
The PCB foam on the
rear end is 1.3mm
away from the edge
of the avoidance slot
The PCB foam on the
front end is 1.1mm
away from the edge
of the avoidance slot
1.1mm
1.3mm
40mm

## Slide 14
RV-2FR
5. The key components
5.2 Robot
1
13
unit：mm
Maximum lifting weight 最大可搬重量 | 3KG
Arm length 臂長 | 504mm
Positional repeatability 位置重複精度 | ±0.02mm
Accuracy of software algorithm 软件算法精度 | ±0.02
位置重複精度 =±0.02mm；
Positional repeatability =±0.02mm；
組裝精度=位置重複精度 +下蓋CCD识别精度+PCB CCD识别精度+软件算法精度：±（0.02+0.0025+0.0025+0.02）=0.045mm。
Assembly accuracy = Positional repeatability + front housing CCD identification accuracy + PCB CCD identification accuracy+softwarealgorithmaccuracy:±(0.02+0.0025+0.0025+0.02) =0.045mm。

## Slide 15
5. The key components
5.3 Material Fetching Component
14
1
unit：mm
Upper CCD
Nozzle
light source

## Slide 16
5. The key components
5.4 Feeder
Reclaiming area
Schematic of coil material
Note: It is recommended to manually wipe and clean the bidding platform with a dust-free cloth once per shift.
Material-sensing optical fibers
Bid dispenser | 
category | 120-Forward push type bid dispensing machine (standard machine）
UPH | 1s/pcs
The maximum diameter of the coil | 76mm
Maximum strip width | 69.855mm
The quantity of a single roll of material | estimate500
2
15
unit：mm

## Slide 17
5. The key components
5.5 Upper CCD
1
unit：mm
layout：
350±10mm
50±10mm
camera lens：FL-CC1214A-2M
camera：FM-GE500-22M
optical source：DRL-80W
PCBA
Hardware name | Model | quantity
camera | FM-GE500-22M | 1
lens | RICOH/FL-CC2514-2M | 1
Lap pick-up | not | 0
light source | Light source/Hua Zhou/LRS-90W60 | 1
Light source controller | DKZ2-24V-2-AC | 1
Camera mounting orientation | Turn your back to the man-machine↑
The distance between the camera surface → the product | 350±10 mm
The light source → the camera surface | 50±10mm
visual field | 72mm*54mm
Image pixel size | 2592*1944
Camera single-pixel accuracy | 0.028

## Slide 18
5. The key components
UpCCD image processing:
1.UpCCDMark Photo Location
2.Check for putting EMI
3.Check for putting Heat sinks
1.Take Mark1 and Mark2 to calculate the Mark center of the camera to find the position.
The image processing method is NCC Pattern + Fit Circle
Bot Side
CCDUPMark1
CCDUPMark2
2.Check：Whether there is EMI & Heat sinks
The image processing method is Image Statistic / YoloV5 Object Detection
Mark image processing
5.5 Upper CCD
2
Need to change the image from Calla newest panel design Drw, the W reduce from 184mm to 177 mm

## Slide 19
5. The key components
5.5 Lower CCD
unit：mm
layout：
350±10mm
215±10mm
camera lens：FL-CC3516-2M
camera：FM-GE500-22M
optical source： BAR-108W30
material
Heat sinks
Hardware name | Model | quantity
camera | FM-GE500-22M | 1
lens | RICOH/FL-CC2514-2M | 1
Lap pick-up | not | 0
light source | Light source/Hua Zhou/LRS-132W30 | 1
 | Light source/Hua Zhou/BAR-108W30 | 2
Light source controller | DKZ2-24V-2-AC | 1
Camera mounting orientation | Turn your back to the man-machine↓
The distance between the camera surface → the product | 350±10 mm
The light source → the camera surface | 40±10mm
The camera surface → a ring-light source | 215±10mm
visual field | 72mm*54mm
Image pixel size | 2592*1944
Camera single-pixel accuracy | 0.028
optical source：LRS-132W30
40±10mm
3

## Slide 20
5. The key components
DnCCD image processing:
1.DnCCDMark Photo Location
Take Mark1 to calculate the Mark center of the camera and the angle to find the position.
The image processing method is Shape Pattern
5.5 Lower CCD
4
Need to change the Heatsink image of Calla instead of Cony

## Slide 21
20
1
unit：mm
6. The key components
The adsorption surface is customized according to the shape of each excipient
6.1 Feed suction nozzle

## Slide 22
7. Action flow design
Step2: The CCD identifies and locates the Mark point of the PCBA
Step3: The placement head moves to the reclaiming area to pick up the loose heat sheets
Step5: The placement head is moved to the placement area for placement
Step4: The placement head is moved to the lower CCD to identify EMI
21
unit：mm
Step5: The jacking cylinder descends, and the conveyor line at the back section of the PCBA board enters the next process
Step1: The PCBA board of the front transmission line flows in, blocking the cylinder from rising, the sensor in place responds, and the top cylinder rises, and the PCBA link is clamped to block the cylinder from descending

## Slide 23
8. Timing diagram
22
UPH≈3600/(65.5/12)*0.8 ≈520
Note：80% is estimated OEE, only for UPH calculation. not real product data
unit：mm

## Slide 24
Thank you
23