## Slide 1
CNT
2025.06.30
Calgary Press Bot Copper Foil Fixture DFM
Ver 2.0

## Slide 2: Calgary Press Bot Copper Foil Fixture
Summary: The dimension of this fixture is L*W*H=350mm*573mm*471mm.
350mm
471mm
573mm
overview

## Slide 3
Protect
Light curtain
Touch screen
Control button
Air pressure control valve
Power button
Power outlet
Air connector
Regulator
Barometer
Electric control box
Air structure
Electric control module
Calgary Press Bot Copper Foil Fixture
Internet connector

## Slide 4
Press module
Solenoid valve
Press cylinder
Cylinder
Vertical plate（A7075）
Bottom plate
(A7075)
Electric control plate
Backplane（A7075）
Location sensor
Limitation module
PLC
Linear guide
Pressure sensor
Calgary Press Bot Copper Foil Fixture

## Slide 5
Press cylinder size(TR25x50s)
Air pressure | 0.38Mpa
Press force | 37kg
Calgary Press Bot Copper Foil Fixture

## Slide 6
Holder design
Calgary Press Bot Copper Foil Fixture
Press head is 0.5mm larger then copper foil.
X direction
Y direction
The gap between housing and holder is 0.15mm.
Press head design
No interference with housing
Al+1mm rubber, 70A

## Slide 7
Holder and press head alignment
Calgary Press Bot Copper Foil Fixture
Alignment pin.
pin
The press head is aligned with press head plate by pin, then we use alignment pin to do alignment during fixture adjustment.
Press head
Press head plate

## Slide 8
Work procedures
3.Press copper foil
4.Take out device
1.Put housing on holder
Calgary Press Bot Copper Foil Fixture
2.Press start button to start fixture